## Slide 1: Ch.1. The Environmental Isotopes
What is isotopes?
  ISO (same) + TOPE (position)
  Elements having same no of proton (Z), but different no of neutron (N)
  The same elements with different masses (A)
  AZEN (188O10)  Or smiply AE (18O) .

## Slide 2
Types of isotopes
  Stable
  Unstable
  Radiogenic
  Heavy
  Light
  Nontraditional stable
Isotones & isobars ?

## Slide 3
Plot of Z vs. N for nuclides up to tin (Z = 50) showing the’ stable valley’ of the nuclides.
From
www.sprawls.org/ppmi2/RADIOTRANS/
See Fig. 1-1 on p.3

## Slide 4
Magic number of neutron? (2, 8, 28, 50, 82, 126)
What is environmental isotopes?
  The isotopes used in the environmental studies (in the text, especially for the environmental hydrogeological studies)

## Slide 5
Significance of environmental isotopes (in hydrogeology)?
  Trace groundwater provenance
  Estimate groundwater age
  Interpretation of groundwater quality
  Understanding geochemical evolution (reactions and reaction rates) and recharge processes
  Recognizing geochemical & biogeochemical cycles of pollutants among soil-water-atmosphere

## Slide 6
How to express isotopic compositions?
  d = (Rsample-Rstd)/Rstd * 1,000 (‰)
  Where R=(heavier isotope)/(lighter isotope)
  Example:
  d18O = {(18O/16O)sample - (18O/16O)std }/ {(18O/16O)std *1,000
  See Table 1-1 on p.6 for the commonly used stable environmental isotopes

## Slide 7
Stable isotope standards and measurements
  Also See Table 1-1 on p.6.
  Discuss
    The expression of each isotopic compositions
    Standard materials for different isotopes
    Preparation for the measurements (extraction methods)
    Read from p.7 to p.13

## Slide 8
Isotope ratio mass spectrometry (IRMS)
  See Fig. 1-4 on p.14
  Discuss
    The basic instrumentation of mass spectrometer
    What would be the advantage of ratio mass
    How does the carrier gas He (continuous flow inlet) improve the system
    What kind of interface would be possible for the smple inlet (front end) (for example Elemental analyzer or laser ablation)

## Slide 9
General Instrumentation of Mass Spectrometer (TIMS)
From http://www.mhhe.com/physsci/chemistry/carey/student/olc/ch13ms.html

## Slide 10
General Instrumentation of Isotope Ratio Mass Spectrometer
From http://web.sahra.arizona.edu/programs/isotopes/methods/gas.html

## Slide 11
Typical Instrumentation of Accelerator Mass Spectrometer
From http://web2.ges.gla.ac.uk/~dfabel/AMS/AMS_schematic.html